## Slide 1: Elmo: Source-Routed Multicast for Public Clouds
Muhammad Shahbaz
Lalith Suresh, Jen Rexford, Nick Feamster, Ori Rottenstreich, and Mukesh Hira
Notes: Hi, my name is Shahbaz. Today, I am going to talk about our work on Elmo: Source-Routed Multicast for Public Clouds. In this talk, I will show how we scale multicast in public clouds by exploting domain-specific characteristics of datacenters and using programmable software and hardware switches. (next slide)

## Slide 2: Cloud Workloads Exhibit 1-to-Many Comm. Patterns
vSwitch
vSwitch
vSwitch
vSwitch
Notes: Cloud workloads are commonly driven by systems that deliver large amounts (next slide)

## Slide 3: Cloud Workloads Exhibit 1-to-Many Comm. Patterns
Notes: of data to groups of endpoints. (next slide)

## Slide 4: Cloud Workloads Exhibit 1-to-Many Comm. Patterns
Tenants: … and more
Notes: Cloud providers (like Amazon, Google, and Microsof support hundreds of thousands of tenants, each of which may run tens to hundreds of such workloads. (next slide)

## Slide 5: Cloud Workloads Exhibit 1-to-Many Comm. Patterns
Streaming Telemetry
(e.g., Ganglia Monitoring System)
Replication
(e.g., for Databases and state machines)
Distributed Programming Frameworks
(e.g., Hadoop and Spark)
Publish-Subscribe Systems
(e.g., ZeroMQ and RabbitMQ)
Infrastructure Applications
(e.g., VMware NSX and OpenStack)
and more …
Notes: Common workloads include:
(click) streaming telemetry where hosts continuously send telemetry data in incremental updates to a set of collectors,
(click) replication for databases and state machines (e.g., in PAXOS or other consensus algorithms),
(click) distributed programming frameworks (like Spark, and Hadoop),
(click) publish-subscribe systems (like ZeroMQ and RabbitMQ) for publishing messages to multiple receivers,
(click) infrastructure applications (like VMware NSX) running on top of a provider for replicating broadcast, unknown unicast, and multicast traffic.
(click) and more
(next slide)

## Slide 6: Cloud Workloads Exhibit 1-to-Many Comm. Patterns
vSwitch
vSwitch
vSwitch
vSwitch
Multicast
Notes: These workloads naturally suggest the use of (click) native multicast, yet none of the data centers enable (next slide)

## Slide 7: Cloud Workloads Exhibit 1-to-Many Comm. Patterns
vSwitch
vSwitch
vSwitch
vSwitch
Multicast
Notes: it today. (next slide)

## Slide 8: Approaches to Multicast
Control
Overhead
No. of
Groups
Endhost
Overhead
Tenant
Isolation
Bisection
Bandwidth
Run at
Line Rate
IP Multicast
SDN-based Multicast
with rule aggregation
App. Layer Multicast
Traffic
Overhead
Src-Routed Multicast
- SGM
- BIER
Good
Bad
Group
Size
Network
Size
Notes: Existing approaches to multicast are limited in one or more ways, making them infeasible for cloud deployments. For example,
(click) IP Multicast faces lots of control-plane challenges with regard to stability under membership churn, is limited in the number of groups it can support, and can’t utilize the full cross-sectional bandwidth in data centers.
(click) SDN-based Multicast alleviates many of the control-plane issues but is still limited in the number of groups it can support. (click) Increasing the number of groups using flow aggregation, introduces other overheads.
(click) Application-layer solutions are the primary way of supporting multicast in multi-tenant data centers, today. However, these solutions introduce a lot of redundant traffic overhead, impose significant CPU load, and cannot operate at line rate with predictable latencies. Due to these limitations certain classes of workloads (e.g., workloads introduced by financial apps) cannot use today’s cloud-based infrastructure at all.
(click) Existing source-routed solutions (like Bloom Filters and BIER) encode forwarding state inside packets. But, these solutions require unorthodox processing at the switches (like loops) and are not able to process multicast packets at line rate in large networks. (next slide)

## Slide 9: Approaches to Multicast
Control
Overhead
No. of
Groups
Endhost
Overhead
Tenant
Isolation
Bisection
Bandwidth
Run at
Line Rate
IP Multicast
SDN-based Multicast
with rule aggregation
App. Layer Multicast
Traffic
Overhead
Src-Routed Multicast
- SGM
- BIER
Good
Bad
Group
Size
Network
Size
Elmo
Notes: Elmo, on the other hand, is a source-routed multicast solution designed to operate at line rate and introduces negligible traffic overhead while utilizing the entire cross-sectional bandwidth of the data-center network. (next slide)
@Shahbaz: point out that for a solution to be deployable in cloud data centers it needs to address all of the issues listed as columns, above.

## Slide 10: Elmo: Source-Routed Multicast for Cloud Services
Notes: (next slide)

## Slide 11: Elmo: Source-Routed Multicast for Cloud Services
vSwitch
vSwitch
vSwitch
vSwitch
Notes: In Elmo, a (click) software switch encodes (click) the multicast forwarding policy inside packets, (click x2) and network switches read this policy to forward packets to the receivers. (next slide)

## Slide 12: Elmo: Source-Routed Multicast for Cloud Services
Key challenges:
How to efficiently encode multicast forwarding policy inside packets?
How to process this encoding at line rate?
Notes: Thus, there are two key challenges that we need to address … (next slide)

## Slide 13
Core
Spine
Leaf
Hypervisor
Processes:
VMs, containers, etc.
- Symmetric
- Short Paths
- Co-located
Placement
Exploiting DC Characteristics for Efficient Encoding
vSwitch
vSwitch
vSwitch
vSwitch
Notes: Data-center topologies tend to be symmetric; having a layered structure consisting of core, spine, and leaf layers. (click) Second, they have limited number of switches on any individual path. (next slide) Finally, to minimize internal bandwidth use, tenant virtual machines (VMs) tend to cluster in the same part of the data-center topology. (next slide)
Elmo (click) exploits unique characteristics of data-center topologies and tenants’ VM placement to (click) efficiently encode multicast forwarding policy inside packets such as … (next slide)

## Slide 14
PISCES
PISCES
PISCES
PISCES
Programmable Switches for Line Rate Processing
Barefoot Tofino or
Cavium XPliant
Notes: and modern programmable switches to (click) process it at line rate

## Slide 15: Encoding a Multicast Tree in Elmo
Key design decisions:
Encoding switch output ports in a bitmap
Encoding on the logical topology
Sharing bitmap across switches
Dealing with limited header space using default p-rules
Reducing traffic overhead using s-rules
Notes: There are (click) five key design decisions that enable Elmo to generate efficient encoding of multicast trees which is both compact and simple for switches to process at line rate. (next slide)

## Slide 16: Encoding a Multicast Tree in Elmo
Multicast Tree
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
PISCES
PISCES
PISCES
PISCES
Notes: (next slide)

## Slide 17: 1. Encoding Switch Output Ports in a Bitmap
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
10
10
01
01
11
11
1011
1011
1011
1011
Downstream
PISCES
PISCES
PISCES
PISCES
100111
001011
101101
001110
1. Bitmap is an internal data structure in switches for replicating packets
2. Switches typically have many ports participating in a multicast tree or none at all
Notes: @mshahbaz: point out that we only generate the encoding for network switches (and not the software switches).
We use (click) bitmaps for each network switch to specify which ports should forward the packet. Using this is desirable for two reasons: (click) (1) a bitmap is the internal data structure that network switches use to direct a packet to multiple output ports and (2) switches typically either have many output ports in the set or are not even part of the multicast tree. (next slide)

## Slide 18: 1. Encoding Switch Output Ports in a Bitmap
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
10
10
01
01
11
11
1011
1011
1011
1011
Downstream
PISCES
PISCES
PISCES
PISCES
100111
001011
101101
001110
Bitmap + Flag Bit
Upstream
Notes: Second, for switches in the upstream path of the packet (e.g., leaf and spine), we maintain a flag bit (along with the bitmap) to indicate the switch to forward the packet upstream using the configured multipath scheme (e.g., ECMP or CONGA). (next slide)

## Slide 19: 2. Encoding on the Logical Topology
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
10
10
01
01
11
11
1011
1011
1011
1011
PISCES
PISCES
PISCES
PISCES
100111
001011
101101
001110
Core
Spine
Leaf
Notes: Next, we exploit the symmetry in data-center topologies. Core switches and spine switches, in each pod, share the same bitmap, hence, (next slide)

## Slide 20: 2. Encoding on the Logical Topology
Logical Core
Logical Spine
Leaf
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
1011
10
01
11
P0
P1
P2
P3
PISCES
PISCES
PISCES
PISCES
100111
001011
101101
001110
Notes: we group these switches together, as a logical switch, and maintain only one bitmap (and switch ID) for each of these logical switches. (next slide)

## Slide 21: 3. Sharing Bitmap Across Switches
Logical Core
Logical Spine
Leaf
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
100111
001011
101101
001110
1011
10
01
11
P0
P1
P2
P3
001111
L5, L7
p-rule
Clustering Algorithm (a greedy version of Min-K-Union) to determine which switches should share a bitmap while minimizing extra transmissions.
Notes: To further reduce the number of bitmaps we need to encode in the packet, we let switches, on the same layer, share a bitmap by allowing some extra transmissions. For example, (click) L5 and L7 can share a bitmap (which is the bitwise OR) of their individual bitmaps (i.e., 001111). This would generate two extra transmissions: one at L5’s forth port, and the one one at L7’s sixth port.
(click) We wrote a clustering algorithm (a greedy version of MIN-K-UNION) to determine which switches should share a bitmap while yielding minimum number of extra transmissions. (next slide)

## Slide 22: 4. Dealing with Limited Header Space using Default p-Rule
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
100111
001011
101101
001110
1011
10
01
11
P0
P1
P2
P3
p-rule
101111
L0, L6
default p-rule
001111
L5, L7
Notes: There is a fixed number of bitmaps we can encode in the packet header as p-rules. Thus, even after applying the techniques so far, we may still have some switches left. To handle these leftover switches, we introduce the notion of a default p-rule, whose bitmap is the bitwise OR of all the switch bitmaps not assigned a non-default p-rule.
For example, if we have space for only one p-rule and allow only two extra transmissions per p-rule, (click) then L5 and L7 will share the p-rule. (click) L0 and L6 are the leftover switches, which will be assigned to the default p-rule, generating two more extra transmissions. (next slide)

## Slide 23: 5. Reducing Traffic Overhead using s-Rules
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
100111
001011
101101
001110
1011
10
01
11
P0
P1
P2
P3
p-rule
101111
L0, L6
default p-rule
001111
L5, L7
Broadcast
Notes: Default p-rule in the limiting case can lead to a lot of extra transmissions, essentially broadcasting packets from all the switches assigned to it. To reduce the traffic overhead without increasing the packet header size, we exploit the fact that switches already support multicast group tables. Thus, before assigning a switch to a default p-rule, we first check if the switch has space in its multicast group table. If so, we install an entry in the switch (i.e., s-rule), and assign only those switches to the default p-rule which don’t have spare s-rule capacity.
So, in our example, with an s-rule capacity of one, both leaf switches L0 and L6 will have an (next slide)

## Slide 24: 5. Reducing Traffic Overhead using s-Rules
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
100111
001011
101101
001110
1011
10
01
11
P0
P1
P2
P3
001111
L5, L7
p-rule
s-rule entry each
Notes: s-rule entry now, instead of the default p-rule. (next slide)

## Slide 25
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
100111
001011
101101
001110
1011
10
01
11
P0
P1
P2
P3
Encoding a Multicast Tree in Elmo
Notes: So, after applying all the techniques, the encoding for our example will look like the following: (next slide)

## Slide 26
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
001011
101101
001110
1011
10
01
11
P0
P1
P2
P3
Encoding a Multicast Tree in Elmo
Sender
100101-1
00-1
1011
P2,P3:11
P0:10
L5,L7:001111
L0,L6:101111
Parameters: 1 p-rule per downstream layer (2 extra transmissions) and
no s-rules
Default p-rule
100111
Notes: With one p-rule per layer (and no more than two extra transmissions per p-rule) and no s-rules, we will get the encoding like this …
(click x5)
@mshahbaz: point out that downstream p-rules remain the same and only the upstream p-rules are updated per sender. Also, how we don’t need to store ids for the upstream switches.
(next slide)

## Slide 27
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
001011
101101
001110
1011
10
01
11
P0
P1
P2
P3
Encoding a Multicast Tree in Elmo
Sender
100101-1
00-1
1011
P2,P3:11
P0:10
L5,L7:001111
L0,L6:101111
Parameters: 1 p-rule per downstream layer (2 extra transmissions) and
1 s-rule per switch
Default p-rule
100111
Notes: (click) and with additional s-rule capacity, (next slide)

## Slide 28
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
001011
101101
001110
1011
10
01
11
P0
P1
P2
P3
Encoding a Multicast Tree in Elmo
Sender
100101-1
00-1
1011
P2,P3:11
L5,L7:001111
Parameters: 1 p-rule per downstream layer (2 extra transmissions) and
1 s-rule per switch
100111
s-rule entry each
Notes: spine switches in pod P0, and leaf switches (L0 and L6) now have an s-rule entry instead of the default p-rule.
@mshahbaz: point out the difference b/w extra transmissions with and without s-rules.
(next slide)

## Slide 29: Encoding a Multicast Tree
PISCES
PISCES
vSwitch
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
P0
P1
P2
P3
s-rule entry each
Controller
Computes the encoding
1011
P2,P3:11
L5,L7:001111
100101-1
00-1
Elmo Header
Notes: A controller receives join requests from the tenant through (click) an API, provided by the cloud provider, and (click) computes a compact encoding for the multicast tree. The encoding consists of a list of packets rules (or p-rules)---consisting of one or more switch IDs and an output port bitmap along with a default p-rule---which is encapsulated as a header on the packet and switch rules (or s-rules) as a mechanism for reducing traffic overhead.
(click)
The controller installs flow rules on software switches specifying where to the forward and which p-rules to push on the packet,
(next slide)

## Slide 30: Encoding a Multicast Tree
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
P0
P1
P2
P3
Controller
Computes the encoding
flow rules specifying:
output ports and the Elmo header to push on the packet
s-rules
Elmo Header
100101-1
00-1
1011
P2,P3:11
L5,L7:001111

## Slide 31: Encoding a Multicast Tree
PISCES
PISCES
PISCES
PISCES
C0
C1
C2
C3
S0
S1
S2
S3
S4
S5
S6
S7
L0
L1
L2
L3
L4
L5
L6
L7
P0
P1
P2
P3
Controller
Computes the encoding
flow rules specifying:
output ports and the Elmo header to push on the packet
s-rules
Elmo Header
100101-1
00-1
1011
P2,P3:11
L5,L7:001111
Notes: The software switch intercepts the packet originating from the VM. It sends the packet as-is to (click) any neighboring VMs in the tree and (click) pushes the p-rules on the packet before forwarding it to the leaf switch (L0 in this case).
(click x4) Switches in the network find a matching p-rule and forward the packet to the associated output ports. If a packet contains no matching p-rule, the switch checks for an s-rule matching the destination IP address and forwards the packet accordingly.
(click) Finally, software switches receive the packet. By that time all p-rules have been removed from the packet by the network switches. Software switches then forward the packet to the receiving VMs. (next slide)

## Slide 32: Evaluation
We evaluated three main aspects of Elmo:
Data- and control-plane scalability: Elmo scales to millions of multicast groups with minimal flow-table usage and control overhead on switches.
End-to-end applications: Applications run unmodified and benefits from reduced CPU and bandwidth utilization.
Hardware resource requirements: Elmo is inexpensive to implement in switching ASICs.
Load on hypervisor switches: Elmo imposes negligible overheads at hypervisor switches
Notes: add speaker notes. (next slide)

## Slide 33: Elmo Scales to Millions of Groups
For a multi-rooted Clos topology with 27K hosts (having 48 hosts per rack), 1M multicast groups (with groups sizes based on IBM’s WVE trace), and a p-rule header of 325 bytes:
Notes: In (click) a multi-rooted Clos topology with 27K hosts and 1M multicast groups, with group sizes based on a production trace from IBM’s Websphere Virtual Enterprise and p-rule header of 325 bytes:
(click) (i) Elmo can encode, without using default p-rules, 89% of groups when no extra transmission is allowed and up to 99% of groups when this condition is relaxed.
(click) (ii) 95% of switches have less than 4059 rules when no extra transmission is allowed, and maximum of 107 rules when 12 extra transmissions are allowed per p-rule.
(click) (iii) traffic overhead is negligible for cases where we allow extra transmissions and is identical to the ideal multicast, when no extra transmission is allowed.
(next slide)

## Slide 34: Elmo Scales to Millions of Groups
For a multi-rooted Clos topology with 27K hosts (having 48 hosts per rack), 1M multicast groups (with groups sizes based on IBM’s WVE trace), and a p-rule header of 325 bytes:
min (max)
*
*
https://conferences.sigcomm.org/co-next/2013/program/p61.pdf
Notes: Elmo reduces control-plane update overhead on network switches and directs updates to hypervisor switches instead. (next slide)

## Slide 35: Applications Run Unmodified with No Overhead
Subscriber
Publisher
Notes: With unicast, the throughput at subscribers decreases as we increase the number of subscribers because the publisher becomes the bottleneck; the publisher services a single subscriber at 185K rps on average and drops to about 0.25K rps for 256 subscribers. With Elmo, the throughput remains the same regardless of the number of subscribers and averages 185K rps throughout.
(click) The CPU usage of the publisher VM (and the underlying host) also increases with increasing number of subscribers. With Elmo, the CPU usage remains constant regardless of the number of subscribers (i.e., 4.97%)

## Slide 36: Elmo Operates within the Header Size Limit of Switch ASICs
190 bytes for other protocols (e.g., datacenter protocols take about 90 bytes)
Notes: For (click) a baseline switching ASIC that can parse a 512-byte packet header, (click) Elmo consumes only 63.5% of header space even with 30 p-rules, (click) still having 190 bytes for other protocols (e.g., in data-center networks, protocols take about 90 bytes). (next slide)

## Slide 37: Elmo Adds Negligible Overheads to Soft. Switches
Separate write call for each p-rule
Notes: Elmo adds negligible overheads to software switches when encapsulating p-rule headers on the packet. Increasing the number of p-rules reduces the pps rate, as the packet size increases, while the throughput in bps remains unchanged which matches the capacity of the links at 20Gbps. With separate headers, the throughput drops down to about 10Gbps with only 5 p-rules and then tapers off at about 5Gbps with 30 p-rules. (next slide)

## Slide 38: Conclusion
Designed for multi-tenant data centers
Compactly encodes multicast policy inside packets
Operates at line rate using programmable data planes
Elmo
A Scalable Multicast
Service
Notes: In conclusion,
(click)
we presented Elmo, a scalable multicast service. (click) Elmo is designed to be deployable in today’s multi-tenant data centers supporting millions of multicast groups and tenant isolation, while utilizing full cross-sectional bandwidth of the network. (click) Elmo takes advantage of the unique characteristics of data-center topologies and to compactly encode forwarding rules inside packets and (click) process them at line rate using programmable data planes.
(next slide)

## Slide 39
Muhammad Shahbaz
http://cs.stanford.edu/~mshahbaz
Questions?
Please visit our project webpage at:
https://elmo-mcast.github.io
Notes: With this I conclude my presentation. Thank you, and I’m happy to take any questions.