## Slide 1: OVS Conference 2020. OVS benchmark
Dec 2020
Guy Twig & Roni Bar Yanai
NVIDIA

## Slide 2: Agenda
Common switch benchmarks
Networking traffic pattern
Extending benchmark with common case
Results
Worst Case
Best Case

## Slide 3: Common Switch Benchmarks

## Slide 4: Switch Benchmarks
Focus on worst case scenario
Worst Case:
  Fixed packet size 64,128,256,…
  Concurrency of “flows/sessions”, that depends on tested use case
  Round robin or random flow per packet
Internet MIX (IMIX)
  Choosing a mix of packet sizes
  Traffic is still random
  Current studies shows that typical traffic has average of 500 bytes to 800 bytes, with strong appearance on edges
RFC 2544
RFC 8204
VSPERF
Common Practice

## Slide 5: Benchmarks
Not Necessarily:
  Different scenarios have different bottlenecks
  Having max rate on 64 bytes, will not stretch PCI for example
  Max MTU might stretch PCI, but not memory
  Processing time depends on packet size
  Mix if packet sizes can hurt PCI optimizations
100 Gbps require different testing of the infrastructure
  64 bytes packet on 100Gbps is > 148MPPS
  Typical SW switch can support 500kPPS (community) – 2MPPS (optimized) per core (DPDK)
  Host required to allocate 50-100 cores just for forwarding traffic (assuming scale is linear)
  Single session (elephant) can be blocked by core capacity
If I can run in worst case, then I’m good for common right?
Compute resources
Packet delivery resources

## Slide 6: Elephant Flow vs Mice Flow and flow locality

## Slide 7: Elephant vs mice flows
Public traces http://pages.cs.wisc.edu/~tbenson/IMC10_Data.html
Out of the million flows:
100 flows consumed 60% of the bytes
71k consumed 95% percent of the bytes
Observation: Optimizing only ~5% of the flows, can affect more than 90% of the total bytes
Small percentage of the flows consume most of the bytes in the system

## Slide 8: Elephant vs mice flows
Another cited work: Network Traffic Characteristics of Data Centers in the Wild [1]
The authors have analyzed traces from 10 different data centers, having web services, file storage, line of business application, customer enterprise application and data intensive applications such as map-reduce.
Data centers we commercial, private enterprise and campus
Most of the flows are less than 10kbytes
10% of the flows consumed most of the data
Packet size is clustering around 200 bytes and 1440 bytes
New flow rate: 2%-20% of the flows opened with 10 micro interval
The number of active sessions within a time frame was much smaller than the overall concurrent flows
Small percentage of the flows consume most of the bytes in the system
[1] BENSON, T., ANAND, A., AKELLA, A., AND ZHANG, M. Understanding Data Center Traffic Characteristics. In Proceedings of ACM WREN, 2009

## Slide 9: Elephant vs mice flows
Analysis of TCP Flow Characteristics [2]
In this work, flow characteristics were analyzed 2009-2011 and 2015-2016
Number of flows is higher by ratio and behavior is the same
Long lived flows consumed 90%-95% of the bytes and that haven’t changed
Long flow duration became longer
Inside the Social Network’s (Datacenter) Network [3]
Social network was analyzed
70% of the flows were less than 10kbytes, and median flow size was less than 1kbytes
Looking on single msec, 15-30 flows consumed more than 50% of the bytes
On 5 msec time frame there were only 1000 active sessions
Elephant vs Flows haven't changed match
[2] X Cui, X Xu, Q ShenLi, X Liang - International Conference on Computer, Network, Communication and Information Systems (CNCI 2019)
[3] A. Roy, H. Zeng, J. Bagga, G. Porter, and A. C. Snoeren. Inside the social network's (datacenter) network. SIGCOMM'15, pages 123–137.

## Slide 10: Elephant Flow vs mice flows
TCP nature of sending a batch of packets on every acknowledgment generates bursts within the flows
Research have shown that on a small-time frame only fraction of the flows are in fact active
Locality also fits the elephant vs mice nature of traffic; big flows need throughput and for that TCP window size should be high. Big TCP window generates locality
Strong Locality

## Slide 11: Locality in Video
Traffic record were taken on client. It is assumed that on server locality is even stronger. RTT to server was less than 5msec
8 packets within 10 micro received
Client ack, 400 micro
6 packets within 5 micro received
8 packets within 9 micro received

## Slide 12: Locality in Video
Youtube are using QUIC as transport layer. Shows similar behavior as TCP
5 packets within 3 micros
QUIC acknowledge packets
2 packets in less than a micro
5 packets in less than 3 micro

## Slide 13: Locality and caching
100Gbps
Looking on 10 microseconds time frame
Limited to 1950 packets of size 64 bytes
Limited to 244 packets of 512 bytes
Locality:
Even small cache can assure that locality shown withing 10 microseconds is supported
Modern caches that can support thousands of concurrent flows will show benefit
M=time slot in micro.
total-packets-msec = max_bps/8/ packet-size/((10^6)/M)

## Slide 14: Active Flows Video
Video traffic is active only 10%-20% of the time
It is shown that the client flows are active only part of the time (in seconds)
Server might have 5-10 times concurrent “big” flows but only 10%-20% will be active on a specific second
Only fraction will be active on microsecond
Video is mostly ABR – Adaptive bit rate

## Slide 15: Active Flows social media
Video traffic is active only 10%-20% of the time
Recorded on client
Going over feed of Facebook
Shown strong locality
Like video (some content is video)

## Slide 16: Active Flows Browsing
Less locality is shown both on active sessions and a bit less on TCP level
Still locality was high and shown 2-6 TCP packets withing 10 micro
10 biggest flows out of 1900 flows consumed 70% of the bytes

## Slide 17: Conclusions
Typical traffic shows a strong locality on the microsecond level
Flows with strong locality are also the flows that consume most of the bytes
Only 10%-20% of the consuming flows are active on a second time frame
Most of the flows are very small and ends with less than 10kbytes

## Slide 18: Common case Use Cases
Testing caching strategic, for example testing EMC vs. SMC
Testing HW offload benefit, where typically CPU is busy with small flows open rate and HW still handle the large flows
Offload and optimization strategic
Infrastructure planning

## Slide 19: Testing
Notes: Thanks Roni.
I’m Guy Twig from the SW performance team.
Now we are going to talk about our testing

## Slide 20: Benchmark setup
We use Trex due to its availability as SW traffic generator.
VM
testpmd
CPU
RAM
100GbE
Drivers
Kernel
NVIDIA BlueField-2 DPU
Port 1
Port 2
TREX
Packet Generator
Port 2
Port 1
OVS-DPDK
Notes: The topology we choose to use in the benchmark is as the following:
The DUT is BlueField-2 DPU connected B2B to another host with TREX installed as SW traffic generator
On The ARM, OVS-DPDK with HW offload and configured with VxLAN and connection tracking rules/
On the VM side we are using testpmd as a forwarder.
For OVS-DPDK we are using in 4 cores
The setup is performance tuned

## Slide 21: Traffic stream
pkt1 | … | pkt1 | pkt2 | … | pkt2 | … | pktN
Elephant Stream
N – how many different packets in stream
M – Locality number – how many same packets in a row
N*M – Total number of packets in Elephant Stream
The size of each packet in elephant stream is 1400B
M
pkt1 | pkt2 | … | pktn
Mice Stream
N – how many different packets in stream between row packets
The size of each packet in mice stream is 64B/128B/256B
N
Stream Calculation Example:
Stream Type | Locality | Flows | Packet Size (B) | Total Bytes
Elephant stream | 8 | 1,000 | 1400 | 11200
8 * Mice stream | 1 | 100,000 | 64 | 512
6 * Mice stream | 1 | 100,000 | 128 | 768
6 * Mice stream | 1 | 100,000 | 256 | 1536
Total stream sequence size = 11200 + 8*64 + 6*128 + 6*256 = 14016B
Total stream sequence = 8 + 1*8 + 1*6 + 1*6 = 28 pkts
Average packet size = 14016/28 = 500B
Theoretic MPPS for 100Gb/s = 100*10^9/((500+20)*8) = 24.01 MPPS
Elephant Stream has 80% Bytes from all the stream
Notes: As Roni mentioned we separated the stream for two streams, elephant stream and mice stream.
The main idea is that the elephant stream holds something like 1K flows with 1400B packet size. The stream doesn’t have much packets, but in overall it holds from 70-80% of the total Bytes stream
Also it holds a locality number that represent the number of packets that will be in a row (for better caching).
The Mice stream has many packets but overall holds only up to 30% of total Bytes.
Each mice stream has many different packets with 128B or 256B packet size.
For the testing we used 1 Elephant stream with 1440B and 1K flows, 5 mice streams with 128B and 5 mice stream with 256B. Each mice stream has 30K different packets

## Slide 22: Locality vs. worst case
Tested Stream
Elephant Stream: N=1K ;M=10
Mice Stream: N=10
1 Elephant stream with 1K flows and locality 10. – packet size 1440B
5 * mice streams with 30K flows – packet size 128B
5 * mice streams with 30K flows – packet size 256B
Chart: Stream with Locality vs. Stream without Locality - 300K connections - VxLAN Traffic + Connection Tracking Rules
| M=1 | M=10
Forwarding rate [Mpps] | 16.8041 | 18.0042
Line Rate [%] | 88.18 | 93.15
Notes: ES_pkt1*10-MS1_128_pkt1-MS1_256_pkt1-MS2_128_pkt1-MS2_256_pkt1…ES_pkt2*10-MS1_128_pkt2-MS1_256_pkt2-MS2_128_pkt2-MS2_256_pkt2…

## Slide 23: HW offload vs SW VirtIO
SW VirtIO tested with 4 cores and over ConnectX-6 Dx
Chart: HW Offload vs Not Offload - 450K connections - VxLAN Traffic + Connection Tracking Rules
| SW VirtIO | HW Offload
Forwarding rate [Mpps] | 1.1502 | 18.0042
Line Rate [%] | 6.0249 | 94.3123
Tested Stream
Elephant Stream: N=1K ;M=10
Mice Stream: N=10
1 Elephant stream with 1K flows and locality 10. – packet size 1440B
5 * mice streams with 30K flows – packet size 128B
5 * mice streams with 30K flows – packet size 256B

## Slide 24: Summary
We could only achieve dozens of microseconds inter gap and not microseconds as defined
Still showed that small locality of 4-8 packets of less than 30% of the overall packets had 7%-10% impact in PPS and throughput
We think that once we can generate better locality we can reach line rate in such scenario
Setting a more realistic scenario can focus in creating the right optimizations
Having real case scenario can show the real saving in cores when using HW offload
In the future we plan to combine such test with open-rate creating full realistic scenario
  long elephant flows opening and closing
  mice flows opening and closing