## Slide 1: OpenFlow Representation of Encapsulation Metadata

## Slide 2: Mapping Geneve Option to an OXM
0
15
16
24
31
oxm_class
oxm_field
vendor id / experimenter id
oxm_length
HM
23
22
0
15
16
27
31
option class
type
Variable length data (max 124 bytes)
length
23
R
oxm_class = 0xffff (experimenter oxm)
oxm_field = ONFOXM_ET_TUN_METADATA.
oxm_length includes experimenter id, so max length when HM = 1 is (255 – 4) / 2 = 125
  However if MSB of experimenter id is non-zero, max length when HM = 1 is (255 - 1) / 2=127
Encode Geneve Length into oxm_length and handle one Geneve option per oxm.
  This makes a Geneve option (128 – 1) = 127 bytes and would fit the OXM.
Other alternatives
  Can we get oxm_classes for Geneve option class registry ?
  Reduce Geneve type space from 8 to 7 bits ?
variable length payload (max 127 bytes)

## Slide 3: OVS infrastructure changes
We start with a short demo and code flow to highlight the changes.
Our tunnel configuration
root@noiro-ucs06:~/demo-scripts# ovs-vsctl show
cf02d4b4-d5d7-4c63-a823-880e135328df
Bridge "br0"
Port "br0"
Interface "br0"
type: internal
Port "vmtap100"
Interface "vmtap100"
Port geneve
Interface geneve
type: geneve
options: {remote_ip=flow}

## Slide 4: Demo
ovs-ofctl -OOpenFlow13 add-flow br0 "in_port=1, tun_id=0x32, tun_src=12.1.1.1 tun_metadata=ab1234cddeadbeefab1234cddeadbeef/ffff00ff, actions=output:2”
We need to be able to support multiple of tun_metadata= matches and set actions in a single flow mod.
Each tun_metadata= option maps to a single OXM of variable length.
The value itself is transparent to the infra code except for some validations.
root@noiro-ucs06:~/ovs-geneve# ovs-appctl ofproto/trace br0 "recirc_id(0),tun_id=0x32,tun_src=12.1.1.1,tun_dst=12.1.1.6,tun_metadata=ab1234cddeadbeefab12,in_port(1)"
Bridge: br0
Flow: tun_src=12.1.1.1,tun_dst=12.1.1.6,tun_tos=0,tun_ttl=0,,in_port=1,vlan_tci=0x0000,dl_src=00:00:00:00:00:00,dl_dst=00:00:00:00:00:00,dl_type=0x0000
Rule: table=0 cookie=0 tun_id=0x32,tun_src=12.1.1.1,tun_metadata=ab12xxcd/ffff00ff,in_port=1
OpenFlow actions=output:2
Final flow: tun_src=12.1.1.1,tun_dst=12.1.1.6,tun_tos=0,tun_ttl=0,,in_port=1,vlan_tci=0x0000,dl_src=00:00:00:00:00:00,dl_dst=00:00:00:00:00:00,dl_type=0x0000
Megaflow: pkt_mark=0,recirc_id=0,tun_id=0x32,tun_src=12.1.1.1,tun_dst=12.1.1.6,tun_metadata=ab12xxcd/ffff00ff,tun_tos=0,tun_ttl=0,,in_port=1,dl_type=0x0000
Datapath actions: 3
I am representing wildcard don’t care bytes with xx in the final flow.

## Slide 5: Little bit of OVS internals.
ofctl context (can also come come via OpenFlow FlowMod)
  parse_ofp_str__ parse FlowMod string and build a match structure
  {
  for each type=value in the command line
  mf_parse() maps type to mf_field
  mf_from_tun_metadata_string()
  mf_set() sets value in match
  match_set_tun_metadata_masked()
  }
  ofputil_put_ofp11_match build ofpbuf to send to vswitchd.
  {
  oxm_put_match
  nx_put_raw
  for each field in match, append to ofpbuf its nx_match format.
  }

## Slide 6: Little bit of OVS internals.
vswitchd context
  handle_flow_mod
  {
  ofputil_decode_flow_mod decode flowMod buffer and construct a match structure (within struct ofputil_flow_mod)
  ofputil_pull_ofp11_match
  oxm_pull_match
  nx_pull_raw
  for each oxm in the FlowMod message
  nx_pull_match_entry extract mf_field, mf_value and mask
  check for duplicates
  mf_are_prereqs_ok check prereqs for mf_field
  mf_set set value in match
  }
  Once we have a populated ofputil_flow_mod struct, we proceed to add_flow()
  This flow is looked up on a miss upcall (tunnel key constructed via odp_tun_key_from_attr)
  In case a set tunnel action is specified the corresponding action is build via
  odp_put_tunnel_action -> tun_key_to_attr
  handle_upcalls() then installs datapath flows in a batch.

## Slide 7: What exists
Working geneve encapsulation in the datapath.

## Slide 8: Infrastructure extensions
mf_field assumes fixed length fields.
  This should be extended so the parse specifies the length. For fixed length field the parsed length == mf->n_bytes.
A field may only appear once in a flow mod.
  mf_set needs to be extended to set a value at an offset within the match field. The offset is the output of parse. For fields that can appear only once the offset will always be 0.

## Slide 9: Infrastructure extensions
struct flow sparse representation limits its size to 252 bytes.
  separate flow_tnl and struct flow. flow_tnl would be variable length depending on the metadata.
  Implications on the classifier. Two lookups per match ?
Geneve pkt can contain upto 252 bytes of option data. flow_tnl.metadata should be able to accommodate this max.

## Slide 10: ofctl / dpctl apis
How do we support adding and dumping options that could be pretty big ?
  Only show bits that are relevant and do not show wildcard bits.

## Slide 11: Geneve critial and non critical options
We will install a drop flow if a critical option is present in the packet and the corresponding flow is not found.
How do we handle unsupported non-critical options.
  Can we add a new configuration bitmask that specifies what options are supported by a tunnel endpoint ? AND during lookup we only check these options (and log the ones that are present and not supported)

## Slide 12: Next steps
Can we implement Geneve support in phases ?
Implement infrastructure extensions needed for Geneve first.

## Slide 13: Questions / Feedback.