## Slide 1: Open vSwitch for Microsoft Hyper-V Eitan Eliahu, Nithin Raju, Ankur Sharma Network & Security Business Unit

## Slide 2: Agenda
Project Introduction
Hyper-V Switch extensions framework
Introduction to NDIS framework
Internals of OVS for Hyper-V
Fun stuff

## Slide 3: OVS on Hyper-V, What is all about?
Develop Open vSwitch on the Hyper-V platform
Shared effort of Cloudbase and VMware
Weekly IRC meeting for discussions
  Tuesday 10 AM PST on #openvswitch

## Slide 4: Design Objectives ...
Interoperable with other Hypervisors
User cross platform common code
Extensible Netlink protocol for user/kernel interface
Windows specific OS primitives for threads, synchronization, and system IOCTL calls
Leverage Switch Extension Framework for enforcing packet forwarding

## Slide 5: Design Objectives
Leverage WFP callout filter driver
Zero copy of packet data in Datapath
Support various tunneling protocols
Asynchronous I/O, NDIS Framework, Event driven notification for Missed packets and port state changes
Use host IP stack for fragment reassembly

## Slide 6: High Level Architecture
Child Partitions (Guest)
OVS Forwarding Extension
I
N
G
R
E
S
S
E
G
R
E
S
S
Hyper-V extensible switch
Interface device
Flowtable
Packet Processing
WFP Callout Driver
Virtual Machine #1
Virtual Machine #2
VIF
VIF
Physical NIC
ovs-vswitchd
netlink socket(emulation)
User
NDIS Stack
Root Partition (Host)
ovs-*ctl
Netlink Message Impl.
Kernel
dpif-
netlink
netdev-
windows
Hyper-V Internal NIC
vport table

## Slide 7: Hyper-V Extensible Switch - Overview
Layered instances of NDIS filter drivers (“switch extensions”) for monitoring, modifying and forwarding
Each layer has an upper “miniport” interface and a lower “protocol” interface.
Packet (NBLs) are forwarded through modifying or inserting ports in the packet forwarding context (OOB).
Packets are transferred through the filter driver in an asynchronous fashion

## Slide 8: Hyper-V Extensible Switch Architecture
MSDN Documentation

## Slide 9: Packet Flow in Hyper-V Virtual Switch
Child Partitions (Guest)
I
N
G
R
E
S
S
E
G
R
E
S
S
Hyper-V extensible switch
Virtual Machine #1
Virtual Machine #2
VIF
VIF
Physical NIC
1
2
3
5
5
NDIS Stack
Hyper-V Internal NIC
1
Packet Injected to Ingress path
Packet sent to extension
Packet sent to miniport edge of switch
Packet shows up on Egress path
Packet sent to destination VM or Physical NIC
4

## Slide 10: Typical Ingress Packet Flow with OVS
OVS extension gets packet from Hyper-V Extensible Switch
OVS extracts a “flow key” for that packet and looks up flow
If a match is found (typical case)the flow destination ports are set into the packet “forward context” of the NBL
If no match packet sent to usermode via upcall
In turn, user mode processes the packet and will send it back to the driver as a raw data. (a new flow is installed)
Driver allocates a new packet and injects into ingress path
If the destination port is a Tunnel port the packet is encapsulated and sent to the external port

## Slide 11: High Level Architecture
Child Partitions (Guest)
OVS Forwarding Extension
I
N
G
R
E
S
S
E
G
R
E
S
S
Hyper-V extensible switch
“OpenvSwithDevice” device
Flowtable
Packet Processing
WFP Callout Driver
Virtual Machine #1
Virtual Machine #2
VIF
VIF
Physical NIC
ovs-vswitchd
1
2
3
4
4
netlink socket(emulation)
User
NDIS Stack
Root Partition (Host)
ovs-*ctl
Netlink Message Impl.
Kernel
dpif-
netlink
netdev-
windows
Hyper-V Internal NIC
1
vport table

## Slide 12: Kernel Datapath - About
OVSEXT - NDIS Filter driver implementing forwarding extensions
Compiled using Visual Studio 2013
Documentation in datapath-windows/DESIGN
Notes: Filter driver sits in-between the Switch’s protocol edge, and the Switch’s Miniport edge

## Slide 13: Kernel Datapath - Components ...
Interfacing with NDIS stack
Registers drivers with NDIS upon load
OVS datapath created/deleted when OVS extension is enabled/disabled on a Hyper-V switch
Supports single OVS datapath
Control path - OID callbacks
Datapath - Ingress, and Ingress completion
Notes: Creation and Initialization of the datapath ie. Flowtable creation, Enumeration of the ports on the Hyper-V switch etc happen when the OVS extension is enabled on the Hyper-V switch.
Datapath is not created from the userspace unlike on other platforms.

## Slide 14: Kernel Datapath - Components ...
Interfacing with OVS Userspace
Control device for Userspace to talk to kernel datapath
Netlink sockets emulated in userspace using handles to control device
Netlink message handling in kernel datapath
Netlink commands in openvswitch.h supported, with extensions defined in OvsDpInterfaceExt.h
Notes: Netlink PID generated by OVS kernel datapath

## Slide 15: Kernel Datapath - Components ...
Port management
OVS-port-name is identity of port in Datapath & OVSDB
Port enumerated on the Hyper-V switch need to be “activated” by adding it from OVS userspace
Hyper-V internal port attached to the Host IP stack
  Used as VTEP
Port Event notifications - create/delete/update

## Slide 16: Kernel Datapath - Components ...
Optimized Buffer (NBL) management
Avoid deep-copies of NBLs. Works by keeping ref count to parent NBLs, and shallow copying MDLs
Zero copy in the OVS extension
Tunneling
IP Helper for ARP resolution & Route lookup
VXLAN tunnelling supported. Easy to extend
Flowtable/Actions
  Supports all basic actions including set L2/L3

## Slide 17: Kernel Datapath - Components ...
NIC Offloads completion (VIF NIC)
Checksum and TSO completion in Transmit direction
Checksum verification in Receive direction
Packet send/miss to userspace
Packet notification to avoid busy polling in userspace

## Slide 18: Userspace - Components ...
Posix code ported to Windows
Netlink sockets emulated
Unified DPIF provider for Linux & Windows
  Uses pool of netlink sockets per handler (thread)
Netdev-Windows implemented using netlink commands in kernel datapath

## Slide 19: Userspace - Components
PowerShell cmdlet
Set the “OVS-Port-Name” of a port to name in OVSDB, so datapath can map the Hyper-V port to OVS port
Windows specific command line utility
Eg. Set-VMNetworkAdapterOVSPortDirect
-VMname Ubuntu-VM
-OVSPortName vif-port-1

## Slide 20: Open vSwitch for Microsoft Hyper-V
Project Introduction
Hyper-V Switch extensions framework
Introduction into NDIS framework
Internals of OVS for Hyper-V
Fun stuff - Demo
  Install the OVS kernel driver
  Configuring OVS
  Ping between VMs across VXLAN backed tunnel

## Slide 21: Demo
TOPOLOGY

## Slide 22: Developer credits
Ankur Sharma
Ben Pfaff
Eitan Eliahu
Guolin Yang
Gurucharan Shetty
Linda Sun
Nithin Raju
Saurabh Shah
(and more)
Alin Serdean
Lucian Petrut
Samuel Ghinet
Sorin Vinturis
Questions?

## Slide 23: Backup Slides

## Slide 24: Hyper-V Extensible Switch - Overview
MSDN Documentation

## Slide 25: Main Functional Modules
Switch Forwarding Extension
  Layered filter driver
WFP Callout driver - used for decapsulation of tunneled packets
Two control paths
  Extensible User/Kernel mode interface through exposing a “Netlink” device interface
  NDIS/WMI control path through OIDs
Remote VTEP IP address through the use of the host stack (IP Helper)
Network Buffer management (avoids packet data copy)

## Slide 26: OVS Switch Forwarding Extension Driver
Registers with NDIS as a filter driver upon loading
Implemented as a set of callback functions adhere to “NDIS Filter Driver” interface
  Callback for Egress and Ingress packet processing
  Packet processing is done on the egress path
  Callback for Port and Nic creation and state change
  Callbacks for processing control commands (OIDs)
Acts as a “Miniport” for an upper layer filter driver
  Indicates received packets to upper layer
  Callback for packet returned from upper layer
Acts as a “Protocol” for lower layered filter driver
  Send sdoen packets originated from upper layer
  Callback upon packet send completion

## Slide 27: OVS Switch Forwarding Extension Driver - cont.
Each Hyper-V Virtual Switch is associated with a Device Object, OVS uses a single Device Object (datapath) for all OVS Virtual Switches
Forwarding is performed on the ingress path on Filter Send NBL callback
Packets can be dropped, offload completed and indicated to usermode, Cloned and forwarded to Vport(s), Encapsulated and sent to a Tunnel port, VLAN tagged
Packet / NBL processing is based on NDIS service function which creates new fragmented NBL based on an original NBL (No data copying rather than buffer control structure manipulation)

## Slide 28: WFP Callout Filter Driver - Tunnel Packet Processing
Installed as a filter driver on the Host network stack
Packed into the same binary as the extension driver
Registers a Datagram “callout” with the stack filter engine for processing fragmented packets received on a tunnel UDP port
The filter engine calls the driver ClassifyFn callback function for network packets associated with callout rule
Packet is intercepted and removed from the host stack
The packet is decapsulated and processed and it was received on the egress callback of the Extension driver
Non fragmented tunnel packets are intercepted and processed directly

## Slide 29: Userspace - Components [...]
Netdev-windows
No native netdev support
Supports “system” and “internal” ports
Messy to use Windows APIs like GetAdaptersInfo()
Netdev commands implemented in kernel datapath
  Get MAC address, MTU, etc
  No support for packet send, receive etc (not needed)

## Slide 30: High Level Architecture
Child Partitions (Guest)
I
N
G
R
E
S
S
E
G
R
E
S
S
Hyper-V extensible switch
Virtual Machine #1
Virtual Machine #2
VIF
VIF
Physical NIC
1
2
3
4
4
NDIS Stack
Hyper-V Internal NIC
1
The built in switch calls the extension Send callback function to process a set of packets originated by a VM
The extension (indirectly) calls the lower driver on its Send callback passing the packets.
The packets are transferred to the destination VM over the VM Bus
The lower layer driver on the destination VM indicates the packet to the Extension.
The Extension (indirectly) calls the upper layer driver with the packet.
Upper layer driver return the packet to the extension
In turn the extension return the packet to the lower driver
Packet return is propagated to the source VM
Send complete callback is called on the extension

## Slide 31: Typical Ingress Packet Flow
An “enlightened” or emulated Virtual NIC driver in a guest transfers a packet originated by the VM to the Virtual Switch over the VM Bus.
The Hyper-V Extensible Switch passes the packet to the Extension with a source port associated with the VM VNIC.
The filter driver generates a “flow key” for that packet.
The flow key is matched to a cached flow table
If a match is found (typical case) the flow destination ports are set into the packet “forward context” of the NBL
If a match is not found the packets is “terminated”, packed in a Netlink format and indicated up to usermode.

## Slide 32: Typical Ingress Packet Flow cont.
In turn, user mode (vswitchd.exe) processes the packet and will send it back to the driver as a raw data. (a new flow is installed)
The driver allocates a new packet structure and process it as it was received on its ingress callback
if the destination port is a Tunnel port the packet is encapsulated and sent to the external port