## Slide 1: OpenVswitch Performance measurements & analysis
Madhu Challa

## Slide 2: Tools used
Packet Generators
  Dpdk-Pktgen for max pps measurements.
  Netperf to measure bandwidth and latency from VM to VM.
Analysis
  top, sar, mpstat, perf
  Netsniff-ng toolkit
I use the term flow interchangeably. Unless otherwise mentioned flow refers to a unique tuple < SIP, DIP, SPORT, DPORT >
Test servers are Cisco UCS C220-M3S servers with 24 cores. 2 socket Xeon CPUs E5-2643@3.5 GHz with 256 Gbytes of RAM.
NIC cards are Intel 82599EB and XL710 (support VXLAN offload)
Kernel used is Linux 3.17.0-next-20141007+

## Slide 3: NIC-OVS-NIC (throughput)
Single flow / Single core 64 byte udp raw datapath switching performance with pktgen.
  ovs-ofctl add-flow br0 "in_port=1 actions=output:2"
  Standard OVS 1.159 GBits / sec / 1.72 Mpps
    Scales sub-linearly with addition of cores (flows load balanced to cores) due to locking in sch_direct_xmit and ovs_flow_stats_update).
    Drops due to rx_missed_errors.
    Ksoftirqds at 100%
    ethtool -N eth4 rx-flow-hash udp4 sdfn.
    service irqbalance stop.
    4 cores 3.5 Gbits / sec.
    Maximum achievable rate with many flows 6.8 Gbits / sec / 10 Mpps, and it would take a packet size of 240 bytes to saturate a 10G link.
  DPDK OVS 9.9 Gbits / sec / 14.85 Mpps.
    Yes this is for one core.
    Latest OVS starts a PMD thread per numa node.
  Linux bridge 1.04Gbits / sec / 1.55 Mpps.
 | STANDARD-OVS | DPDK-OVS | LINUX-BRIDGE
Gbits / sec | 1.159 | 9.9 | 1.04
Mpps | 1.72 | 14.85 | 1.55

## Slide 4: NIC-OVS-NIC (latency)
 | OVS | DPDK-OVS | LINUX-BRIDGE | NIC-NIC | VM-OVS-OVS-VM
TCP | 46 | 33 | 43 | 27 | 72.5
UDP | 51 | 32 | 44 | 26.2 | 66.4
Latency measured using netperf TCP_RR and UDP_RR.
Numbers in micro seconds per packet.
VM – VM numbers use two hypervisors with VXLAN tunneling and offloads,
details in later slide.

## Slide 5: Effect of increasing kernel flows
Kernel flows are basically a cache.
OVS performs very well so long as packets hit this cache.
The cache supports up to 200,000 flows (ofproto_flow_limit).
Default flow idle time is 10 seconds.
If revalidation takes a long time, the flow_limit and default idle times are adjusted so flows can be removed more aggressively.
In our testing with 40 VMs, each running netperf TCP_STREAM, UDP_STREAM, TCP_RR, UDP_RR between VM pairs (each VM on one hypervisor connects to every other VM on the other hypervisor) we have not seen this cache grow beyond 2048 flows.
The throughput numbers degrade by about 5% when using 2048 flows.

## Slide 6: Effect of cache misses
To stress the importance of the kernel flow cache I ran a test completely disabling the cache.
may_put=false or ovs-appctl upcall/set-flow-limit.
The result for the multi flow test presented in slide 3.
  400 Mbits / sec, approx 600 Kpps
  Loadavg 9.03, 37.8%si, 7.1%sy, 6.7%us
  Most of these due to memory copies.
    - 4.73% 4.73% [kernel] [k] memset
    - memset
    - 58.75% __nla_put
    - nla_put
    + 86.73% ovs_nla_put_flow
    + 13.27% queue_userspace_packet
    + 30.83% nla_reserve
    + 8.17% genlmsg_put
    + 1.22% genl_family_rcv_msg
    4.92% [kernel] [k] memcpy
    3.79% [kernel] [k] netlink_lookup
    3.69% [kernel] [k] __nla_reserve
    3.33% [ixgbe] [k] ixgbe_clean_rx_irq
    3.18% [kernel] [k] netlink_compare
    2.63% [kernel] [k] netlink_overrun

## Slide 7: VM-OVS-NIC-NIC-OVS-VM
Two KVM hypervisors with a VM running on each, connected with flow based VXLAN tunnel.
Table shows results of various netperf tests.
  VMs use vhost-net
  netdev tap,id=vmtap,ifname=vmtap100,script=/home/mchalla/demo-scripts/ovs-ifup,downscript=/home/mchalla/demo-scripts/ovs-ifdown,vhost=on -device virtio-net-pci,netdev=vmtap.
  /etc/default/qemu-kvm VHOST_NET_ENABLED=1
Table shows three tests.
  Default 3.17.0-next-20141007+ kernel with all modules loaded and no VXLAN offload.
  IPTABLES module removed. (ipt_do_table has lock contention that was limiting performance)
  IPTABLES module removed + VXLAN offload.

## Slide 8: VM-OVS-NIC-NIC-OVS-VM
 | TCP_STREAM | UDP_STREAM | TCP_MAERTS | TCP_RR | UDP_RR
DEFAULT | 6752 | 6433 | 5474 | 13736 | 13694
NO IPT | 6617 | 7335 | 5505 | 13306 | 14074
OFFLOAD | 4766 | 9284 | 5224 | 13783 | 15062
Throughput numbers in Mbits / second.
RR numbers in transactions / second.
Interface MTU was 1600 bytes.
TCP message size 16384 vs
UDP message size 65507.
RR uses 1 byte message.
The offload gives us about 40% improvement for UDP.
TCP numbers low possibly because netserver is heavily loaded.
(Needs further investigation)

## Slide 9: VM-OVS-NIC-NIC-OVS-VM
Most of the overhead here is copying packets into user space and vhost signaling and associated context switches.
Pinning KVMs to cpus might help.
NO IPTABLES
  26.29% [kernel] [k] csum_partial
  20.31% [kernel] [k] copy_user_enhanced_fast_string
  3.92% [kernel] [k] skb_segment
  4.68% [kernel] [k] fib_table_lookup
  2.22% [kernel] [k] __switch_to
NO IPTABLES + OFFLOAD
  9.36% [kernel] [k] copy_user_enhanced_fast_string
  4.90% [kernel] [k] fib_table_lookup
  3.76% [i40e] [k] i40e_napi_poll
  3.73% [vhost] [k] vhost_signal
  3.06% [vhost] [k] vhost_get_vq_desc
  2.66% [kernel] [k] put_compound_page
  2.12% [kernel] [k] __switch_to

## Slide 10: Flow Mods / second
We have scripts (credit to Thomas Graf) that create an OVS environment where a large number of flows can be added and tested with VMs and docker instances.
Flow Mods in OVS are very fast, 2000 / sec.

## Slide 11: Connection Tracking
I used dpdk pktgen to measure the additional overhead of sending a packet to the conntrack module using a very simple flow.
This overhead is approx 15-20%

## Slide 12: Future work
Test simultaneous connections with IXIA / breaking point.
Connection tracking feature needs more testing with stateful connections.
Agree on OVS testing benchmarks.
Test DPDK based tunneling.

## Slide 13: Demo
DPDK test.
VM – VM test.