## Slide 1: OVS DPDK VXLAN & VLAN TSO, GRO and GSO Implementation and Status Update
Yi Yang @ Inspur Cloud

## Slide 2: Goals To Achieve
1
To run OVS DPDK in Openstack production environment
To support UFO (UDP Fragmentation Offload) for VM
To support GRO (Generic Receive Offload) and GSO(Generic Segment Offload) for VLAN and VXLAN
To support VXLAN TSO (TCP Segmentation Offload)
To support VXLAN UFO (some NICs can do this)
VM-to-VM TCP can reach line speed in VXLAN case
VM-to-VM UDP can reach line speed in VXLAN case

## Slide 3: Implementation Status: UFO Done
2
root@ubuntu:~# ethtool -k ens3 | grep udp
udp-fragmentation-offload: on
tx-udp_tnl-segmentation: off [fixed]
root@ubuntu:~#
qemu-system-x86_64 -enable-kvm -nographic -m 4096 -cpu host -smp 2\
-object memory-backend-file,id=mem0,size=4G,mem-path=/dev/hugepages,share=on \
-numa node,memdev=mem0 \
-netdev type=tap,id=tap1,ifname=tap1,script=no,downscript=no,vhost=on,queues=2 \
-device virtio-net-pci,host_mtu=1450,mac=52:54:00:12:34:56,netdev=tap1,\
csum=on,guest_csum=on,guest_ecn=on,guest_tso4=on,guest_tso6=on,\
gso=on,host_ufo=on,guest_ufo=on,mq=on,vectors=6,rx_queue_size=1024 \
xenial-server-cloudimg-amd64-disk.img
VM:
qemu parameters:

## Slide 4: Implementation Status: IPv4 GRO and GSO Done
3
VLAN TCP GRO (DPDK has supported since 17.11)
VXLAN TCP GRO (DPDK has supported since 17.11)
VLAN TCP GSO (DPDK has supported since 17.11)
VXLAN TCP GSO (DPDK has supported since 17.11)
VLAN UDP GSO (DPDK has supported since 17.11)
VLAN UDP GRO (Done by me, 20.11)
VXLAN UDP GRO (Done by me, 20.11)
VXLAN UDP GSO (Done by me, 20.11)
TBD: IPv6 GRO and GSO

## Slide 5: Implementation Status: VXLAN TSO patch ready
4
Most important factor to achieve VM-to-VM TCP line speed
Many NICs can support VXLAN TSO: XL710 (i40e), E810 (ice), ConnectX(mlx4, mlx5), etc.

## Slide 6: Implementation Status: VXLAN UFO (TBD)
5
Some NICs support UFO and VXLAN UFO (igc, e810, txgbe)
UDP should have better performance than TCP, but not in fact,
The major reason is TCP can be offloaded but UDP can’t

## Slide 7: Implementation Status: TCP and UDP performance
host2
host1
6
Non-openstack, no conntrack, no other openflow entry except default entry
 | TCP (Gbps) | UDP (Gbps, -l 8192) | UDP (Other)
current | 8.08 | 3 | 2.2 (-l 1478)
VXLAN TSO | 9.02 | 9.83 (UFO) | 6 (non-UFO, -l 8192)
VM1
VM2
OVS DPDK
br-int
OVS DPDK
br-int
dpdkvhostuserclient
dpdkvhostuserclient
VXLAN
VXLAN
eth1
eth1

## Slide 8: Implementation Status: TCP and UDP performance
7
Non-openstack, conntrack
 | TCP (Gbps， no conntrack) | TCP (Gbps，conntrack)
current | 8.08 | 5.76
VXLAN TSO | 9.02 | 5.44
table=0, priority=10,ct_state=-trk,ip,nw_src=10.15.2.0/24 actions=ct(table=0)
table=0, priority=10,ct_state=+new+trk,ip,nw_dst=10.15.2.9 actions=ct(commit),output:1
table=0, priority=10,ct_state=+est+trk,ip,nw_dst=10.15.2.9 actions=output:1
table=0, priority=10,ct_state=+new+trk,ip,nw_src=10.15.2.9 actions=drop
table=0, priority=10,ct_state=+est+trk,ip,nw_src=10.15.2.9 actions=output:vxlan0
table=0, priority=1,ct_state=-new-est+trk,ip,nw_dst=10.15.2.9 actions=drop
table=0, priority=0 actions=NORMAL

## Slide 9: Implementation Status: line speed TCP and UDP (almost done)
Chart: OVS DPDK VM-to-VM Performance in non-openstack (Gbsp, no ct)
| TCP Performance | UDP Performance
current | 8.08 | 3
VXLAN TSO | 9.02 | 9.83
8

## Slide 10: Implementation Status: TCP Performance with CT
9
Chart: OVS DPDK vm-to-vm TCP Performance (Gbps)
| TCP (no ct) | TCP (ct)
current | 8.08 | 5.76
VXLAN TSO | 9.02 | 5.44

## Slide 11: Implementation Status: TCP and UDP performance
10
Openstack：
Openstack floating IP:
 | TCP (Gbps) | UDP (Gbps) | UDP (Other)
OVS 2.9.5 | 2.32 | 2.49 (no UFO) | 
VXLAN TSO | 7.49 | 5.28 (UFO) | 2.15 (no UFO)
 | TCP (Gbps) | UDP (Gbps)
OVS 2.9.5 | 0.134 | 0.120
VXLAN TSO | 5.10 | 1.55

## Slide 12: Implementation Status: TCP and UDP in Openstack
Chart: OVS DPDK VM-to-VM Performance in Openstack (Gbps)
| TCP Performance | UDP Performance
current | 2.32 | 2.49
VXLAN TSO | 7.49 | 5.28
11

## Slide 13: Implementation Status: floating IP Performance
Chart: VM-to-VM Floating IP Performance in OVS DPDK in Openstack (Gbps)
| TCP Performance | UDP Performance
current | 0.134 | 0.12
VXLAN TSO | 5.1 | 1.55
12

## Slide 14: Implementation Status: tap/veth performance
13
No PMD
PMD
 | veth-to-veth TCP (Gbps) | veth-to-veth UDP (Gbps) | tap-to-tap TCP (Gbps) | tap-to-tap UDP (Gbps)
No PMD | 6.28 | 1.59 | 19.6 | 2.2
PMD | 22.2 | 3.5 | 27.3 | 3.7

## Slide 15: Implementation Status: tap/veth performance
Chart: veth-to-veth Performance (Gbps)
| TCP Performance | UDP Performance
no PMD | 6.28 | 1.59
PMD | 22.2 | 3.5
14
Chart: tap-to-tap Performance (Gbps)
| TCP Performance | UDP Performance
No PMD | 19.6 | 2.2
PMD | 27.3 | 3.7

## Slide 16: Implementation Status: interface stats and status
15

## Slide 17: Implementation Status: known issues
16
GRO can dramatically boost performance when conntrack/security group is used
GSO performance isn’t good, need to be optimized
BIG ISSUE: tap in namespace won’t work after ovs-vswitchd is restarted
tap&veth performance has big drop when PMD thread has many tap&veth interfaces to handle
Multi-segmented mbuf support (rejected before because of crash)
Userspace conntrack and some other stuff have big impact on performance from openstack performance data
IPv6 GRO & GSO (TBD)

## Slide 18: Summary
17
VXLAN TSO is very great feature
OVS DPDK is on the way to Openstack production environment
There are still some road blocks to be removed
  Multi-segment mbuf support
  GRO and GSO
  PMD support for veth & tap
  restart issue for tap