## Slide 1
Break through
Bottlenecks of OVS and Virtio
by Using Smart NIC and vDPA Offload
Yi Yang @ Inspur Cloud

## Slide 2
Agenda
OVS and virtio Performance Bottleneck
Solutions to Performance Bottleneck
Hardware Offload (Smart NIC and vDPA)
How to Enable SF and vDPA in Openstack
Performance Comparison
Future Work
Demonstration

## Slide 3
OVS and virtio Performance Bottleneck
Kernel data path: skb not cache friendly
Virtio: memory copy, in-kernel vhost thread, ksoftirqd
Single queue/single thread does have performance celling
Multiqueue will consume too many CPU cores
It’s unacceptable for VM networking to consume precious compute resources.

## Slide 4
OVS and virtio Performance Bottleneck (cont’d)
memcpy copy from VM to tap port
memcpy copy to VM from tap port

## Slide 5
OVS and virtio Performance Bottleneck (cont’d)
send side: pert top -p <vhost-PID>

## Slide 6
OVS and virtio Performance Bottleneck (cont’d)
receive side: pert top -p <vhost-PID>

## Slide 7
OVS and virtio Performance Bottleneck (cont’d)
receive side: pert top -p <ksoftirqd>

## Slide 8
OVS and virtio Performance Bottleneck (cont’d)
send side compute node: Linux kernel pktgen with 10 Tx threads

## Slide 9
OVS and virtio Performance Bottleneck (cont’d)
receive side compute node for Linux kernel pktgen with 10 Tx threads

## Slide 10
send side compute node: iperf client with 16 threads
OVS and virtio Performance Bottleneck (cont’d)

## Slide 11
OVS and virtio Performance Bottleneck (cont’d)
receive side compute node: iperf with 16 threads

## Slide 12
OVS and virtio Performance Bottleneck (cont’d)
Chart: single thread/single queue pps (iperf3 result, unit: 10k per second)
| OVS kernel | AWS M5 | Alicloud
single thread/single queue pps (10k per second) | 17.1 | 39.5 | 45

## Slide 13
Solutions to Performance Bottleneck
Solutions to Kernel datapath
  OVS DPDK
  Hardware offload (smart NIC: tc flower for kernel, rte_flow for userspace)
Solutions to virtio
  VM CPU tunning: nova config: cpu_mode = host-model | host-passthrough
  Pin vCPU: nova config: vcpu_pin_set=1-7,9-15
  Use hugepage for VM
  VM kernel parameter optimization: mitigations=off
  Tx zero copy: vhost_net module parameter, experimental_zcopytx=1
  Hardware offload: smart NIC, vDPA

## Slide 14
Hardware Offload (Smart NIC and vDPA)
Smart NIC
  Offload VXLAN encap & decap
  Offload dataplane (tc datapath)
  conntrack offload (including NAT)
vDPA (virtio data path acceleration)
  Decouple control path and dat path of virtio
  Standadize VF/SF controlplane and dataplane
  Use virtio interface to achieve SR-IOV performance
  Virtio full hardware offload
  Support live migration
  Requirement: NIC driver needs a vDPA add-on

## Slide 15
qemu
virtio-net driver
vDPA framework
vendor specific vDPA driver
VF/SF (Scalable Function): vDPA device
NIC
Kernel space
user space
applications
virtio control plane
vendor specific control plane
virtio data plane
Hardware Offload (Smart NIC and vDPA) (cont’d)

## Slide 16
SF (Scalable Function/Sub Function)
  SF is lightweigh, no full PCI config space, reset, registers
  SF is deployed one by one, but all the VFs are deployed once
  Has own capabilities and resources, e.g. rx, tx queues
  has dedicated window in PCI BAR space
  No special BIOS settings
  Can co-exist with SR-IOV
  Needn’t enable SR-IOV
  supports tc offloads
  share PCI level resources (e.g. PCI MSI-X IRQs) with other scalable functions or its parent PCI function.
Hardware Offload (Smart NIC and vDPA) (cont’d)

## Slide 17
Hardware Offload (Smart NIC and vDPA) (cont’d)

## Slide 18
Prerequisites:
  Linux kernel: >= 5.17
  Mellanox OFED package: >= 5.5-1.0.3.2
  Mellanox ConnextX-6 Ln | Dx | Bluefield
  qemu >= 6.2.0: --enable-vhost-vdpa
  libvirt >= 8.2.0
  iproue2-next: git://git.kernel.org/pub/scm/network/iproute2/iproute2-next.git
  neutron: needs a patch from Sean Mooney in neutron master
  neutron_lib: needs a patch from Sean Mooney in neutron_lib master
  vif_plug_ovs: needs a hacking patch to support SF
  nova: needs 8 nova patches, 7 from Sean Mooney in nova master
  Note: all the patches are https://github.com/yyang13/ovsconf-2022/
How to Enable SF and vDPA in Openstack (cont’d)

## Slide 19
Install Linux kernel (>= 5.17):
  CONFIG_MLX5_ESWITCH=y, CONFIG_MLX5_SF=y, CONFIG_VDPA=m, CONFIG_MLX5_VDPA=y, CONFIG_VHOST_VDPA=m
Install Mellanox OFED package (cold reboot needed)
  https://network.nvidia.com/products/infiniband-drivers/linux/mlnx_ofed/
Enable SF (cold reboot needed)
  mlxconfig -d 0000:06:00.0 s PF_BAR2_ENABLE=0 PER_PF_NUM_SF=1 PF_TOTAL_SF=252 PF_SF_BAR_SIZE=10 SRIOV_EN=0
Add udev rules for renaming interface name:
  https://github.com/Mellanox/scalablefunctions/wiki/Upstream-step-by-step-guide#311-setup-udev-rule-file
Install iproute2-next: vdpa tool
How to Enable SF and vDPA in Openstack (cont’d)

## Slide 20
Install qemu>=6.2.0, libvirt>=8.2.0
Patch Openstack Neutron, Nova, neutron_lib, vif_plug_ovs
  https://github.com/yyang13/ovsconf-2022
  Reboot neutron server, nova-api, nova-compute
Enable switchdev mode
  devlink dev eswitch set pci/0000:07:00.1 mode switchdev
Add SF:
  devlink port add pci/0000:07:00.1 flavour pcisf pfnum 1 sfnum 89
  devlink port function set pci/0000:07:00.1/98304 hw_addr fa:16:3e:9f:44:88
  ip link set dev en7f1pf1sf89 up
  devlink port function set pci/0000:07:00.1/98304 state active
How to Enable SF and vDPA in Openstack (cont’d)

## Slide 21
Load vdpa modules:
  modprobe vdpa
  modprobe vhost_vdpa
  modprobe mlx5_vdpa
Unbind rdma and netdevice for SF device
  echo mlx5_core.rdma.2 > /sys/bus/auxiliary/devices/mlx5_core.sf.2/mlx5_core.rdma.2/driver/unbind
  echo mlx5_core.eth.2 > /sys/bus/auxiliary/devices/mlx5_core.sf.2/mlx5_core.eth.2/driver/unbind
Add vdpa device:
  vdpa dev add name vhost-vdpa-0 mgmtdev auxiliary/mlx5_core.sf.2 max_vqp 16
How to Enable SF and vDPA in Openstack (cont’d)

## Slide 22
Openstack create vdpa port
  openstack port create --network private --host eip02 --vnic-type vdpa --mac-address fa:16:3e:9f:44:88 vdpa1
  openstack port create --network private --host eip03 --vnic-type vdpa --mac-address fa:16:3e:9f:44:89 vdpa2
Disable security group and port security
  openstack port set --no-security-group vdpa1
  openstack port set --disable-port-security vdpa1
  openstack port set --no-security-group vdpa2
  openstack port set --disable-port-security vdpa_port2
Create vDPA VM on host “eip02” and “eip03”:
  openstack server create --image ubuntu-18.04 --flavor m1.xxxlarge --port vdpa1 --availability-zone :eip02 --wait vm02-vdpa1
  openstack server create --image ubuntu-18.04 --flavor m1.xxxlarge --port vdpa2 --availability-zone :eip03 --wait vm03-vdpa2
How to Enable SF and vDPA in Openstack (cont’d)

## Slide 23
Number of Thread: number of Tx threads/Tx CPU cores
Nonoffload pps: no offload, other_config:hw-offload=false
Pin offload pps: offload enabled, other_config:hw-offload=true, Tx thread/Tx vCPU is pinned to physical core
offload pps: offload enabled, other_config:hw-offload=true, no cpu pin
Ideal offload pps: offload enabled, other_config:hw-offload=true， linearly scalable
Performance Comparison
Number of Thread | nonoffload pps | pin offload pps | offload pps | ideal offload pps
1 | 206466 | 456620 | 543494 | 543494
2 | 405980 | 779111 | 872120 | 1086988
3 | 598144 | 1080067 | 1268574 | 1630482
4 | 786855 | 1371746 | 1482786 | 2173976
5 | 978230 | 1485557 | 1667188 | 2717470
6 | 1165530 | 1702001 | 1867117 | 3260964
7 | 1263961 | 1908726 | 2003145 | 3804458
8 | 1264760 | 2005238 | 2077100 | 4347952
9 | 1087676 | 2088526 | 2104596 | 4891446
10 | 1018677 | 2085864 | 2115143 | 5434940
AWS M5: 395,000
Alicloud: 450,000
Offload: 543,494

## Slide 24
Chart: SmartNIC and vDPA Offload Performance
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
nonoffload pps | 206466 | 405980 | 598144 | 786855 | 978230 | 1165530 | 1263961 | 1264760 | 1087676 | 1018677
pin offload pps | 456620 | 779111 | 1080067 | 1371746 | 1485557 | 1702001 | 1908726 | 2005238 | 2088526 | 2085864
offload pps | 543494 | 872120 | 1268574 | 1482786 | 1667188 | 1867117 | 2003145 | 2077100 | 2104596 | 2115143
ideal offload pps | 543494 | 1086988 | 1630482 | 2173976 | 2717470 | 3260964 | 3804458 | 4347952 | 4891446 | 5434940
Performance Comparison (cont’d)

## Slide 27
Future Work
Verify live migration
Investigate and fix conntrack offload issues
Support Katacontainer (both VM and container use Openstack neutron virtual network)
Roll out in production environment

## Slide 28
Demo
https://github.com/yyang13/ovsconf-2022/blob/main/2022-10-25-15-22-11.mp4?raw=true
https://github.com/yyang13/ovsconf-2022/blob/main/2022-10-26-15-06-14.mp4?raw=true

## Slide 30: Thank you!!!